## Slide 1: Fundamental Acoustics
In Wall And Room Structures
Copyright © 2010 – Shannon D. Near – All Rights Reserved

## Slide 2: Acoustics – It’s Not Rocket Science!
It’s actually much harder! Rocket science deals primarily with well understood physics and mathematical formulas surrounding thrust, trajectory, time and distance.
Acoustics deals with complex environments with an infinite number of variables in a very dynamic environment.
So…… Don’t sweat it!! Understanding a few terms and concepts will allow you to answer the vast majority of the questions you will ever be asked regarding acoustics. Remember, the person asking the question probably doesn’t know the answer either.

## Slide 3: Acoustics – Why Bother?
Acoustics, If Understood On Even An Elementary Level, Can Add High Value To Any Building Material Selection Discussion
Acoustics Are A Major Factor In Modern Construction Decisions And Are One Of The Least Understood Areas Of Design
Poor Acoustics Can Ruin An Otherwise Beautiful Wall Installation
In Many Cases, Building Codes Now Require An Acoustical Assessment

## Slide 4: Primary Terms
Sound
Is an oscillating wave of pressure which can travel through solids, liquids, and gases and is within a frequency range and of sufficient power level to be perceived by receptive organs.

## Slide 5: Primary Acoustic Terms
Frequency
Measured in Hertz (Hz) and is the number of wave cycles of sound per time, usually a second. The higher the frequency, the higher the perceived pitch.
Pitch
The perceived sensation of sound frequencies as interpreted by the brain in a scale from high to low. Pitch is subjective and can be influenced by the environment, distortion, reflections, movement, etc.

## Slide 6: The Audible Spectrum
20Hz – 20,000Hz
The human ear is typically capable of hearing between 20z – 20kHz
Females can usually hear slightly higher frequencies than males
Frequencies above 20kHz are ultrasonic
Frequencies below 20Hz are infrasonic
The human voice is usually in the 500Hz to 3500Hz range and is where the majority of acoustic tests are centered

## Slide 7: Now For The Really Hard Stuff!
Decibel (db)
A logarithmic unit that expresses intensity or power of something. In acoustics it measures Sound Pressure Level (SPL) as compared to a reference level (0db). 0 db is not dead silent!
In humans, the ratio of SPL intensity causing permanent damage to the quietest perceived sound is over a trillion so it is expressed logarithmically base 1012 = 12 which is expressed as 0-120 (db)
Every -10db is half as loud

## Slide 8: Common db Levels
Decibel (db)
Rain 40 db
Normal Conversation 60 db
Busy Traffic 85 db
Rock Concerts 105 db
Maximum I-pod Volume 115 db
Gunshots 140 db
Long Term Safety Threshold
Permanent Damage Threshold

## Slide 9: Primary Terms
Reflections
The condition where sound bounces off a surface(s) before reaching the receiver.
Reverberation
The continued reflections of sound within an enclosed space after the sound source has stopped. Long delays are called discreet echoes.

## Slide 10: Primary Terms
STC – Sound Transmission Class
Number rating of a wall or structures ability to block the transfer of sound
NRC – Noise Reduction Coefficient
Number rating which categorizes the sound absorptive or reflective properties of a material or environment

## Slide 11: STC – Privacy Anyone?
STC – Sound Transmission Class
It is the primary way to infer how isolated a room or environment is relative to other rooms.
General Guidelines
30-35 STC = Loud talking understood
40-50 STC = Loud talking not easily understood but may have occupant awareness
60+ STC = Loud talking not audible

## Slide 12: STC – What’s The Big Deal?
Behind The Scenes Voodoo
Generally measured by gathering transmission loss data along 16 different frequencies from 125Hz-4000Hz
Centered on human voice frequencies
Does not cover low frequency industrial noise, music, etc.
Example: If an 80db sound on one side of wall is reduced to 50db on the other the STC is 30
Remember every -10db = ½ as loud!

## Slide 13: STC – Design With Confidence
Considerations
Most codes require minimum of 40 STC in commercial installations
It is harder to block low frequencies than high frequencies as the wave form is much more powerful and longer
Adding mass to the partition wall along with decoupling and insulation will vastly improve STC
Beware of flanking paths!

## Slide 14: STC – FLANKING PATHS
Common Flanking Paths
Ceiling And Floor Joists
Common Duct Work
Missing Or Poor Fitting Door Sweeps
Back-To-Back Electrical Or Utility Boxes In Same Stud Cavity
Outlet Gaps

## Slide 15: STC – Improve Your Ratings
Gain Weight And Isolate
Decouple And Add Length To The Ventilation
Double The Wallboard
Insulate The Stud Cavity
Insulate The Ceiling Plenum & Floor Plenum
Seal All Flanking Paths
In Extremely Sensitive Areas Use Double Walls With Dead Head Ventilation
Plan Ahead For Today & Tomorrow

## Slide 16: NRC – What’s All The Noise About?
Noise Reduction Coefficient
Number rating which categorizes the sound absorptive or reflective properties of a material or environment

## Slide 17: NRC – Doesn’t Tell You Everything
Noise Reduction Coefficient
Is just an average of mid range frequencies (usually 250Hz, 500Hz, 1000Hz, and 2000Hz) rounded to the nearest 5% shown as a decimal.
0.0 = Perfectly Reflective
1.0= Perfectly Absorbent

## Slide 18: NRC – Be Careful
Number Can Be Misleading
Does Not Rate A Materials Ability To Absorb High And Low Frequencies
Averaging Allows For Different Materials To Have The Same Rating But Different Frequency Bias
Does Not Have Any Relevance To A Materials STC Rating

## Slide 19: NRC – Common Ratings
Absorptive Ratings
Brick .00-.03
Wood .05-.15
Heavy Carpet .30-.55
18oz Drapery .60-.65
Fiberglass 3.5” .80-.90

## Slide 20: NRC – Control The Reflections
Don’t Strive For Perfectly Absorbent
Most People Do Not Desire A Room That Is Totally Absorbent
A Little Reverb Is Usually A Good Thing
Angular Geometry Can Be A Good Alternative When Highly Absorbent Materials Cannot Be Used
Avoid Parallel Low NRC Walls

## Slide 21: Acoustics 101 – You Made It!
You Now Have The Tools To Answer Most Of The Acoustic Questions That You Will Ever Be Asked
Do Not Be Afraid To Contact An Acoustician With Questions, Most Love To Talk About It
Remember
Acoustics…. It’s More Than Just Sound

## Slide 22: Fundamental Acoustics
In Wall And Room Structures
Copyright © 2010 – Shannon D. Near – All Rights Reserved