## Slide 1
VIEW SERIES Track Assembly & Installation

## Slide 2
1) VIEW Top/Bottom Universal Track 2) Track Guide
3) Level Adjusters
4) Glass Shims
5) Glass Caulk/Glazing Spline
6) Sliding Glass Door: (3 Sliding Carriages, 1 Bar Pull, 2 Door Stops)
7) Side Glass
Minimum Parts Using Existing Walls
1) Top/Bottom Track
2) Track Guide
6) Sliding Glass Door
3) Level Adjusters
4) Glass Shims
5) Glass Caulk / Glazing Spline
7) Side Glass
Detail of Sliding Carriage:
INCLUDES: 3 sliding carriages (see detail above), 2 door stops, & 1 bar pull.

## Slide 3
FINAL ASSEMBLY
VIEW SERIES
VIEW TRACK
MINIMUM AIR GAP 3/16TH INCH
GLASS SHIM
TRACK GUIDE
TRACK GUIDE
MINIMAL AIR GAP 3/16TH INCH
VIEW TRACK
X
GLASS CAULK/Glazing spline
GLASS

## Slide 4
TRACK GUIDE
LEVEL ADJUSTER
MINIMUM AIR GAP 3/16TH INCH
VIEW TRACK
TOP TRACK ASSEMBLY

## Slide 5
LEVEL ADJUSTER
GLASS SHIM
BOTTOM TRACK ASSEMBLY
VIEW TRACK
MINIMUM AIR GAP 3/16TH INCH
X
GLASS CAULK/Glazing spline

## Slide 6
VIEW TRACK
MINIMUM AIR GAP 3/16TH INCH
VIEW TRACK
X
GLASS SHIM
GLASS CAULK/Glazing Spline
MINIMUM AIR GAP 3/16TH INCH
1. Are my Tracks Level?
2. Do I have the required Minimum
Air Gap? NOTE: If flooring is not down you
must compensate for its thickness: Min air gap 3/16” + flooring thickness
3. Have I secured the Track Area to
the Deck above the Door
opening?
4. Is the Glass properly secured in
Top Track?
QUESTIONS TO ASK:

## Slide 7
GLASS MEASUREMENT
Measure from the Inside of the Top Track to the Top Edge of the Bottom Track and Subtract 3/16th of an Inch.
Total Distance Minus 3/16”= Glass Length
X
Total minus 3/16th Of One Inch

## Slide 8
GLASS SPACER DETAIL
GLASS SHIM
X
GLASS CAULK/Glazing Spline
Note: Additional Shims can be installed to achieve proper securement in the Top Track.
GLASS CAULK/ Glazing Spline

## Slide 9
TOP TRACK DETAIL WITH GLASS INSTALLED
AIR GAP AT TOP OF GLASS PANEL
Avoid large air gaps by installing additional shims in the Bottom Track.
GLASS

## Slide 10
TRACK GUIDE
VIEW TRACK
VIEW TRACK
TRACK GUIDE
VIEW TRACK
VIEW TRACK
SLIDING DOOR
GLASS MEASUREMENT
Door Glass is measured between the VIEW Top Track and VIEW Bottom Track minus 1/4“
Track Base + Track Base - 1/4 Inch
X
TRACK BASE TO TRACK CEILING MINUS ¼”

## Slide 11
EXISTING WALL
EXISTING WALL
VIEW TRACK
VIEW TRACK
VIEW SERIES
Rough Opening 38 ½”
Side Glass Minimum Width 37”
DIMENSIONS TO ACHIEVE A 33” FINISH OPENING
Glass Door Width 42 ½”

## Slide 12
SLIDING DOOR GLASS TEMPLATE
With Standard Bar Pull
D
TBD
TBD

## Slide 13
SLIDING DOOR GLASS TEMPLATE
With Standard Bar Pull
A
B
C
D
A = Top Left
B = Top Right
C = Bottom Left
D = Door Pull Right
TBD

## Slide 14
EXISTING WALL
EXISTING WALL
VIEW TRACK
VIEW TRACK
VIEW SERIES

## Slide 15: FOR MORE INFO
Contact:
info@nxtwall.com
Or call: 269-488-2752